## Slide 1: Material Transport System
IH JEONG / KOREA
Provide Scalable Management Solution
Revision 1.0.0.0

## Slide 2: Agendas
Structure of MTS
Structure of MCS (Material Control System) Broker
Structure of Transport Job Creator
Structure of Transport Job Database
Structure of Transport Unit Control Manager
Goals of MTS
Applied design concepts

## Slide 3: Structure of MTS
MTS (Material Transport System) 은 역할에 따라서 3 개의 층으로 나눈다.
상위 (MCS Broker Layer)
고객사 MCS (Material Control System) Broker 와 Transport Job Creator 로 구성된다.
중간 (Transport Job Database Layer)
Transport Job 을 유지하고, 상태를 관리한다.
하위 (Transport Unit Control Manager Layer)
Transport Job 을 수행하는 Unit (최대 8대 반송 로봇) 들의 Transport Job 을 제 및 관리한다.
MCS (Material Control System) Broker
Transport Job Creator
Transport Job Database
Transport Unit Control Manager
Transport Unit 1
Transport Unit 2
Transport Unit 3
Transport Unit 4
Transport Unit 5
Transport Unit 6
Transport Unit 7
Transport Unit 8
Upper
Layer
Middle
Layer
Lower
Layer

## Slide 4: Structure of MCS Broker
MCS Broker 의 Remote Commands 별 Task 호출
Customer MCS
Transport Commands
Remote Commands
Is a transport commands ?
Put the transport commands to Job Creator Queue
Is a remote commands ?
Is an activated transport job ?
Check pending transport job list and create process order task
Execute Pause, Resume, or Move order task

## Slide 5: Structure of MCS Broker (Contd.)
Transport unit 의 응답과 이벤트를 MCS 로 전송.
Customer MCS
Report transport job state
Has a notification or response from transport unit ?
Take notification information and send it to MCS.
Is MST connected to MCS ?

## Slide 6: Structure of Transport Job Creator
Transport Job Creator 는 Transport Unit 상태와 Transport Job pending 여부에 따라서, RUN 상태일 경우 항시 Transport Job 을 생성 배정한다.
Is transport unit available?
Has a queued transported job in database ?
Create an acquiring job then put it into transport unit queue.
Is an acquiring job ?
Is a depositing job ?
Create a depositing job then put it into transport unit queue.
Start
Check transport unit state and position then update cache.
Update transport job state in database

## Slide 7: Structure of Transport Job Database
Transport Job Database 는 transport job pushing 이 있을 경우, transport job 을 등록하며, 관리자의 transport job 우선 순위 변경에 pending 순서를 변경한다.
Has a transport job pushing ? or Has a request to update from GUI?
Start
Validate a pushed transport job request.
Insert or Update transport job state in database
Is changed the transport job priority ?
Sort transport job records by priority.

## Slide 8: Structure of Transport Job Database (Contd.)
Transport Job Database 는 transport unit state 가 변경되면, 이를 update 하고, MCS Broker 에게 이를 통지한다.
Has an arrived response codes from transport unit ?
Start
Insert or Update transport unit response and state.
Fire event to notify transport unit state update.

## Slide 9: Structure of Transport Unit Control Manager
Transport Unit Control Manager 는 Transport Job Creator 에 의해 생성된 transport job 을 transport unit controller 에게 전달하고, transport unit controller thread 에 반송 명령을 전달한다.
Has an acquiring transport job for unit ?
Start
Check transport unit state and position
Put transport job order to transmit buffer of transport unit controller .
Has a depositing transport job for unit ?
Check transport unit state and position

## Slide 10: Structure of Transport Unit Control Manager (Contd.)
Transport Unit Controller 의 응답은 transport job database 에 각 transport unit state 테이블에 update 된다.
Has an arrived transport job order ?
Start
Check transport job order and send it to transport unit
Analyze response codes from transport unit and update state of it in database.
Has an arrived response from transport unit ?
Check transport unit state and position
Fire event to notify transport unit state update.
Fire event to notify transport unit state update.

## Slide 11: Goals of MTS
Provides distributed process task by process modules.
Provides stable server modules.
Provides runtime monitoring and service restart features.
Provides extendable transport unit control manager to manage 8 vehicles. (One license supports to control 8 vehicles.)
Provides database server divide from MTS to support heavy transaction.
Provides external schema synchronizing.
Provides transport job Creator and customizing of job creation by option.
Provides MCS Broker interface and customizing.
Notice: The 1st phase goals are Marked items by red color.

## Slide 12: Applied Design Concepts
This project contained general mediator device concept. The detail system structure and implementation plan notes will be added with below technical information.
  MSMQ (Microsoft Message Queue)
  MSSQL Server (Microsoft Database Server Express)
  SECS/GEM specification for AMHS-AGV (Samsung V1.8)

## Slide 13: Data Flow of Transport Unit Control Manager
Transport Unit Control Manager
HTTP Service
Job
Table
Transport Unit 과 Transport Unit Control Manager 간의 데이터 및 상태 정보 연동 흐름도
Job
Transmitter
State
Table
Vehicle State
Manager
Transport Unit 1
HTTP Service
Job
Table
Periodic
State
Reporter
Task
Scheduler
State
Table
Transport Unit 2
HTTP Service
Job
Table
Periodic
State
Reporter
Task
Scheduler
State
Table